## Slide 1: Discrete Choice Models and Behavioral Response to Congestion Pricing Strategies
Prepared for:
The TRB National Transportation
Planning Applications Conference
Mark Fowler & Stacey Falzarano,
Resource Systems Group, Inc.
Kazem Oryani and Cissy Kulakowski,
Wilbur Smith Associates

## Slide 2: Southern California Association of Governments
Nation’s largest MPO
6 Counties
38,000 square miles
19 million residents
550 million daily VMT
20 minutes of delay per driver per day
Today
24 million residents
30 minutes of delay per driver per day
2030
Orange
Riverside
San Bernardino
LA
Ventura
Imperial

## Slide 3: SCAG Express Travel Choices Study
Understand how congestion pricing can be used in the SCAG region to:
Reduce congestion and improve transportation system performance
Improve air quality
Enhance transportation revenues
Objectives
Outreach and public participation
Case studies for existing pricing projects
Update SCAG regional travel demand model to incorporate pricing
  Understand behavioral response to pricing
    Stated preference surveys
Performance and feasibility analysis, develop regional strategy, identify pilot projects, etc...
Approach

## Slide 4: Pricing Strategies Under Consideration
Express Lanes
Single Facility Pricing
Corridor Pricing
Regional Facility Pricing
Cordon Pricing
Area Pricing
Express Parking
VMT Pricing

## Slide 5: Stated Preference Survey
Evaluate the behavioral response of travelers in the region to the 8 different congestion pricing strategies
Estimate proportions of
  Route shift
  Mode shift (HOV, transit)
  Departure time shift
  Changes in destination
  Trip reduction
Estimate traveler values of time (VOT)
Provide inputs to the travel demand model

## Slide 6: Stated Preference Questionnaire
Developed SP questionnaire with four main groups of questions:
  Details of a recent trip in the region
  Trip purpose, time of day, origin, destination, occupancy, frequency, etc.
  Ability to shift destination/time of day
Revealed Trip Characteristics
  How would you travel under hypothetical future conditions that may include pricing?
  Mode, time of day, route, trip reduction
Stated Preference Exercises
  Debrief of SP experiments
  Opinion of pricing strategy, tolling in general
Debrief and Opinion
  Basic household demographics
  Income, gender, age, household size, household vehicles, etc.
Demographics

## Slide 7: What are the behavioral responses for each strategy?
Example trip: Santa Monica to Staples Center
Depart at 6 PM, 14.7 miles, 20-60 minutes
Drive on I-10 Express Lanes and pay toll
Pricing Example 1: Express Lanes on I-10
Drive on I-10 Express Lanes earlier or later (reduced toll)
Drive on I-10 Express Lanes in a carpool (reduced toll)
Drive on I-10 regular lanes (toll free)
Take transit
Don’t make trip
Add tolled Express Lanes to I-10
Discount for off-peak travel
Discount for HOV
GP Lanes remain toll-free
Behavioral response depends on:
  Type of pricing
  Specifics of pricing implementation
  Revealed trip details (origin, destination, time of day, etc.)
Drive to Staples Center and pay toll
Pricing Example 2: Cordon Pricing around Downtown LA
Drive to Staples Center earlier or later (reduced toll)
Drive to Staples Center in a carpool (reduced toll)
Take transit to Staples Center
Don’t make trip
Price all travel into downtown LA
Discount for off-peak travel
Discount for HOV
Change destination?

## Slide 8: Comparison of Behavioral Responses
Pricing Strategy | Don’t Make Trip | Change Destination | Take Transit | Form Carpool | Change Departure Time | Change Route
Single Facility Pricing |  |  |  |  |  | 
Express Lanes |  |  |  |  |  | 
Regional Facility Pricing |  |  |  |  |  | 
Corridor Pricing |  |  |  |  |  | 
Cordon Pricing |  |  |  |  |  | 
Area Pricing |  |  |  |  |  | 
Express Parking |  |  |  |  |  | 
VMT Pricing |  |  |  |  |  | 
Significant impact
Some impact
Minimal impact
X
No impact
X
X
X
X
X
(if applied equally)

## Slide 9: Stated Preference Exercises
Behavioral response information used to develop SP exercises
Each SP exercise presented up to 5 alternatives for making their trip in the future, described by relevant attributes
Attributes varied across all 8 exercises
Each respondent saw two sets of 8 SP exercises for two different pricing strategies
Toll route during the peak
Toll route outside the peak
Toll route in a carpool (HOV)
Alternate route
Alternate destination
Transit
Alternatives
Travel time
Travel cost (toll cost/fare)
Departure time
Occupancy
Mode
Attributes

## Slide 10: Example Stated Preference Exercise: Express Lanes

## Slide 11: Trip Suppression Questions
Ask about trip reduction under a specific travel scenario
Follow-up to find out how trips would be reduced

## Slide 12: Survey Administration and Sample Characteristics
Survey administered online to residents of all six counties
3,590 responses
Each respondent evaluated 2 different pricing strategies
*Census data from the 2009 American Community Survey
Pricing Strategies Evaluated
County of Residence
Chart: 
| Los Angeles | Orange | Riverside | San Bernardino | Ventura | Imperial
Sample | 0.51421 | 0.17604 | 0.12925 | 0.12312 | 0.044847 | 0.012535
Census | 0.54748 | 0.16827 | 0.11816 | 0.11217 | 0.044641 | 0.0092771
Chart: 
| Individual Facility Pricing and Express Lanes | Regional Facility and Corridor Pricing | Cordon/Area Pricing and Express Parking | VMT Pricing
 | 0.29903 | 0.30251 | 0.099025 | 0.29944

## Slide 13: Sample Characteristics
Alternate destination availability
  Differs by trip purpose
Chart: 
| Work Commute | Business-Related | Peak Non-Work | Off-Peak Non-Work
Yes | 0.14234 | 0.15957 | 0.27984 | 0.26
No | 0.72993 | 0.64894 | 0.44033 | 0.44
Unsure | 0.12774 | 0.19149 | 0.27984 | 0.3
Chart: 
| Not at all | Up to 30 minutes | Up to 1 hour | Up to 2 hours | More than 2 hours
Earlier | -0.46379 | -0.28719 | -0.10557 | -0.069916 | -0.073538
Later | 0.38273 | 0.3507 | 0.12618 | 0.072423 | 0.067967
Opinion of pricing strategy
  Opinion decreases as the ability to avoid the toll/fee decreases
Departure time shift
  54% can shift earlier
  62% can shift later
Earlier
Later
Is an alternate destination available for this trip?
Ability to shift departure time earlier or later
Chart: 
| VMT Pricing | Cordon and Area Pricing & Express Parking | Regional Facility & Corridor Pricing | Individual Facility Pricing & Express Lanes
Favor | 0.11163 | 0.13783 | 0.15239 | 0.18817
Neutral | 0.1893 | 0.21941 | 0.19797 | 0.23381
Oppose | 0.69907 | 0.64276 | 0.64963 | 0.57802
Opinion of pricing strategy

## Slide 14: Choice Model Estimation
Multinomial Logit (MNL) models estimated using the SP data
Tested numerous utility specifications
  Variables from the SP experiments (travel time, cost, etc.)
  Revealed trip characteristic variables (trip purpose, time of day, etc.)
  Demographic variables
Models segmented by trip purpose and time of day
Final model specification chosen based on:
  Expected application
  Statistical significance of parameter estimates
  Model fit
  Intuitiveness and reasonableness of the results
Segment | Description
Work Commute | Work commute trips at any time of day
Business-related | Business-related trips at any time of day
Non-work Peak | All other trip purposes during peak hours (6:00 AM – 10:00 AM; 3:00PM – 7:00 PM)
Non-work Off-peak | All other trip purposes during off-peak hours (10:00 AM – 3:00 PM; 7:00 PM – 6:00 AM)

## Slide 15: Choice Model Results
Coefficients specified for:
  Travel time
  Toll cost
  Mode/route specific constants
  Departure shift
  Dummy variables for current HOV/transit users
  Bias removing variables
VOT varies from $6.00 to $20.00 depending on traveler segment and household income
Chart: Annual Household Income
| 10000 | 20000 | 30000 | 42500 | 62500 | 87500 | 112500 | 137500 | 175000 | 225000 | 300000
Work Commute | 10.7007 | 11.7745 | 12.4026 | 12.9421 | 13.5396 | 14.0608 | 14.4501 | 14.761 | 15.1346 | 15.5239 | 15.9695
Business-related | 7.9871 | 10.3914 | 11.7979 | 13.0061 | 14.3439 | 15.511 | 16.3827 | 17.0788 | 17.9154 | 18.7871 | 19.785
Non-work Peak | 5.8748 | 6.4643 | 6.8091 | 7.1053 | 7.4333 | 7.7195 | 7.9332 | 8.1038 | 8.3089 | 8.5227 | 8.7673
Non-work Off-peak | 7.2394 | 9.4187 | 10.6935 | 11.7886 | 13.0012 | 14.0591 | 14.8492 | 15.4801 | 16.2383 | 17.0285 | 17.933
Model Coefficients for Commute Segment

## Slide 16: Sample Model Sensitivities: Express Lanes
Chart: Express Lanes Toll Rate ($/mi)
| 0.1 | 0.2 | 0.30000000000000032 | 0.4 | 0.5 | 0.60000000000000064 | 0.70000000000000062 | 0.8 | 0.9 | 1
Express Lanes | 0.32536 | 0.27906 | 0.23656 | 0.19838 | 0.16474 | 0.13561 | 0.11077 | 0.089882 | 0.072513 | 0.058215
Express Lanes Shift Early | 0.022954 | 0.022422 | 0.021698 | 0.020811 | 0.019794 | 0.018681 | 0.017505 | 0.016296 | 0.015082 | 0.013884
Express Lanes Shift Late | 0.029273 | 0.028576 | 0.02763 | 0.026473 | 0.02515 | 0.023705 | 0.022183 | 0.020622 | 0.019058 | 0.01752
Express Lanes HOV | 0.10336 | 0.10028 | 0.096165 | 0.091224 | 0.085692 | 0.079794 | 0.073732 | 0.067677 | 0.061763 | 0.05609
General Purpose Lanes | 0.47557 | 0.52194 | 0.56618 | 0.60756 | 0.6456 | 0.68003 | 0.71082 | 0.73804 | 0.76192 | 0.78272
Transit | 0.043483 | 0.047723 | 0.051768 | 0.055552 | 0.05903 | 0.062179 | 0.064993 | 0.067483 | 0.069666 | 0.071568
Attribute | Express Lanes | Express Lanes Shift Early | Express Lanes Shift Late | Express Lanes HOV | Regular Lanes | Transit
Travel Time | 35 minutes | 30 minutes | 30 minutes | 40 minutes | 50 minutes | 60 minutes
Toll Cost | $0.10-$1.00/mi | 50% discount | 50% discount | 50% discount | Toll free | $2.00 fare
Shift Amount |  | 60 minutes | 60 minutes |  |  | 
Occupancy |  |  |  | +1 passenger |  | 
Work Commute Segment
Illustrative only
Based on uncalibrated choice model
Results presented for only 1 example trip with the characteristics outlined above
Results do not include interactions with regional network model
Notes

## Slide 17: Sample Model Sensitivities: Area Pricing
Attribute | Current Destination | Current Dest Shift Early | Current Dest Shift Late | Current Dest HOV | Alternate Destination | Transit
Travel Time | 35 minutes | 30 minutes | 30 minutes | 40 minutes | 50 minutes | 60 minutes
Area Pricing Fee | $1.00-$10.00 | 50% discount | 50% discount | 50% discount | Toll free | $2.00 fare
Shift Amount |  | 60 minutes | 60 minutes |  |  | 
Occupancy |  |  |  | +1 passenger |  | 
Chart: Area Pricing Fee ($)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Current Destination | 0.66715 | 0.65056 | 0.63171 | 0.61043 | 0.58656 | 0.55995 | 0.53054 | 0.49834 | 0.4635 | 0.42636
Current Destination Shift Early | 0.029478 | 0.031318 | 0.033097 | 0.034786 | 0.036356 | 0.037777 | 0.039023 | 0.040069 | 0.040896 | 0.041486
Current Destination Shift Late | 0.040006 | 0.042461 | 0.044809 | 0.047009 | 0.04902 | 0.050802 | 0.052322 | 0.053551 | 0.054465 | 0.055049
Current Destination HOV | 0.18736 | 0.1827 | 0.1774 | 0.17143 | 0.16472 | 0.15725 | 0.14899 | 0.13995 | 0.13017 | 0.11973
Alternate Destination | 0.029643 | 0.035119 | 0.041096 | 0.04746 | 0.054059 | 0.060722 | 0.067272 | 0.073553 | 0.079435 | 0.084833
Transit | 0.046361 | 0.057849 | 0.07188 | 0.088881 | 0.10928 | 0.1335 | 0.16186 | 0.19454 | 0.23154 | 0.27254
Work Commute Segment
Illustrative only
Based on uncalibrated choice model
Results presented for only 1 example trip with the characteristics outlined above
Results do not include interactions with regional network model
Notes

## Slide 18: Trip Suppression Model Estimation
Linear regression model
  Dependent variable: percent of trips reduced
  Independent variable: difference in utility (before/after pricing)
  Model included trip distance and household income effects
Work Commute Suppression Results
Non-work Peak Suppression Results
Toll Difference | Travel Time Difference |  |  |  | 
 | 0 | -5 | -10 | -15 | -20
$0.00 | 0.0% | +0.7% | +1.4% | +2.2% | +2.9%
$2.00 | -1.3% | -0.6% | +0.2% | +0.9% | +1.6%
$4.00 | -2.5% | -1.8% | -1.1% | -0.4% | +0.3%
$6.00 | -3.8% | -3.1% | -2.4% | -1.7% | -0.9%
$8.00 | -5.1% | -4.4% | -3.7% | -2.9% | -2.2%
$10.00 | -6.4% | -5.6% | -4.9% | -4.2% | -3.5%
Toll Difference | Travel Time Difference |  |  |  | 
 | 0 | -5 | -10 | -15 | -20
$0.00 | 0.0% | +1.2% | +2.4% | +3.6% | +4.7%
$2.00 | -3.8% | -2.6% | -1.5% | -0.3% | +0.9%
$4.00 | -7.6% | -6.5% | -5.3% | -4.1% | -2.9%
$6.00 | -11.5% | -10.3% | -9.1% | -7.9% | -6.7%
$8.00 | -15.3% | -14.1% | -12.9% | -11.7% | -10.6%
$10.00 | -19.1% | -17.9% | -16.7% | -15.6% | -14.4%

## Slide 19: Trip Suppression Results
Trip Suppression by Income and Trip Distance
  Work Commute Segment
  No travel time difference
  $2.00 toll
Income
Distance (miles)

## Slide 20: Conclusions
Tolling can have a significant impact on travel behavior
The models developed using the survey data indicate that facility pricing and regional facility pricing could substantially affect travel behavior in three ways:
  Time-of-day shifts
  Changes in mode
  Use of express lanes
Similarly the models show that area, cordon, or VMT pricing could, in addition:
  Affect trip destinations
  Cause suppression of trips
These effects can collectively become quite significant as prices increase
Incorporating the survey results into the travel demand model will allow the project team to evaluate a wide range of congestion pricing strategies.

## Slide 21: Contact
Chicago
Vermont
Utah


Mark Fowler
Tom Adler
Stacey Falzarano
Resource Systems Group, Inc.
mfowler@rsginc.com
(802) 295-4999
Kazem Oryani
Cissy Kulakowski
Wilbur Smith Associates
koryani@wilbursmith.com
(203) 865-2191
Thanks to: Annie Nam, Guoxiong Huang, Wesley Hong, and Warren Whiteaker of the Southern California Association of Governments
Notes: 21